## Slide 1: Ethernet-based interconnect, the critical crossroads for HPC & AI networking at scale (exforum112s1)
Eric Eppe
Corporate VP – Portfolio & Strategy HPC/AI/Quantum

## Slide 2: 2023 Best kept secret
HPC & AI/ML have converged characteristics
An Exascale Capable
SuperComputer
An LLM Capable
SuperComputer

## Slide 3: 2023 Best kept secret
HPC & AI/ML have converged characteristics
An Exascale Capable
SuperComputer
A GPT4 LLM Capable
SuperComputer

## Slide 4: 2023 Best kept secret
HPC & AI/ML have converged characteristics
An Exascale Capable
SuperComputer
A GPT4 LLM Capable
SuperComputer
25.000 GPUS
25.000
HS Network Endpoints
100+ racks
1 Trillion Parameters
1 Quintillion Flops
/ 300+ racks*
* Mostly less dense Air Cooled systems

## Slide 5: High Speed Networking for large scale HPC & AI/ML
What are the key criterias to monitor?
Costs
Bandwidth & Latency
SW APIs
HPC
Scalability & topology
QoS
Lossless
Congestion control
AI/ML
Lossless/Lossy
Congestion control
100-400Gb/s (2023)
Sub 300ns P2P latency
Sub 0.9us OSU latency
Higher BW the better
Latency not an issue now (but may be in the future)
RDMA
MPI
OFI
RDMA
NCCL/CUDA/CuDNN
RCCL/ROCm/OneAPI
15/20% of total HW costs in highly dense infrastructure
Higher BW will double costs
ccNUMA
>30% of total HW costs in AirCooled infrastructure
Higher BW will double costs

## Slide 6: High Speed Networking for large scale HPC & AI/ML
What are the key criterias to monitor?
Costs
Bandwidth & Latency
SW APIs
Eviden BXI
Infiniband
(Low Latency Protocols)
HPC
Scalability & topology
RoCE
Infiniband
AI/ML

## Slide 7: Ethernet Based Interconnect
Promises and challenges
COSTS
SCALE
Software
BW & Latency
Ethernet has a vast Ecosystem of components, makers, thus a large volume to decrease costs while increasing speeds
Cost is also a matter of topology & density, higher density = less cabling costs (and vice versa)
Ethernet is not designed for large scale (10s of thousands) coordinated bursty traffic
Very efficient Congestion management is required, hence Lossles and QoS (traffic classes)
RoCE has limitations and large scale RDMA in ScaleUP/ScaleOUT environnement needs an evolution
HPC and AI types of semantics are quite similar (collective operations) and can be implemented on top of existing APIs
Ethernet requires changes to reach low latencies
HPC & AI have different traffic patterns but are using equivalent packet sizes (large)
Low latency is a must for HPC, will be for AI when BW will have reached a limit

## Slide 8: UEC & BXI
Ultra Ethernet Consortium
  EVIDEN is a founding and board member of the UEC
  The only European company in the consortium

## Slide 9: Thanks
Eric Eppe
eric.eppe@eviden.com